## Slide 1
Air Quality Prediction
Predicting the Air Quality Index of Indian cities using regression models
Achalesh Nimbiwal (MS24255), Peehu (MS24191), Vaibhav (MS24090)
IISER Mohali

## Slide 2
Introduction and Objectives
Background
Air pollution is a major environmental concern in India. The Air Quality Index (AQI) summarizes pollution levels in a single number, based on measured pollutant concentrations.
Objectives
Analyze air-quality data from Indian cities.
Predict AQI from pollutant concentrations using three regression models.
Tune the models and compare them using MAE, RMSE, and R².
Build separate next-day AQI models for six cities.

## Slide 3
Dataset
The dataset is India Air Quality Data (2015-2020) from Kaggle.
The file city_day.csv contains one row for each city on each day.
The target variable is AQI.
The inputs for Part I are twelve pollutant measurements.
Group | Pollutants
Particulate matter | PM2.5, PM10
Nitrogen compounds | NO, NO2, NOx, NH3
Gases | CO, SO2, O3
Organic compounds | Benzene, Toluene, Xylene

## Slide 4
Data Preparation
Cleaning
Rows with a missing AQI value were removed.
Missing pollutant values were filled with the median of each pollutant.
The data was checked for null values, duplicate rows, and inconsistent city names.
Feature creation
The Date column was converted to the datetime format.
Year, month, day, and weekday were extracted from the date.
A season label and a winter indicator were added.

## Slide 5
Exploratory Analysis
Yearly average AQI was plotted for every city and for the ten cities with the most records.
Daily and monthly AQI were compared for Delhi, Mumbai, Chandigarh, Bengaluru, Chennai, and Hyderabad from September 2019 to July 2020.
Box plots showed the distribution of each pollutant, and a correlation heatmap showed the relationships between pollutants.
The monthly plots showed a seasonal pattern, with AQI generally lower in the summer months.
These plots do not explain the cause of the seasonal pattern.

## Slide 6
Part I: Models and Settings
The twelve pollutants were the inputs, and AQI was the target.
The data was split 80/20 into training and test sets (random_state = 42).
Hyperparameters of the Decision Tree and Random Forest were tuned with RandomizedSearchCV.
Model | Settings
Linear Regression | Baseline model
Decision Tree | max_depth = 10, min_samples_leaf = 20, min_samples_split = 2
Random Forest | n_estimators = 120, max_depth = 20, max_features = 0.5, min_samples_split = 10, min_samples_leaf = 1, bootstrap = True

## Slide 7
Part I: Results
Model | MAE | RMSE | R²
Linear Regression | 31.17 | 59.44 | 0.807
Decision Tree | 24.45 | 45.21 | 0.888
Random Forest | 20.54 | 40.31 | 0.911
Lower MAE and RMSE and a higher R² indicate better performance.
Random Forest achieved the lowest errors and the highest R².
Linear Regression, the baseline, had the largest errors.
MAE is the average error, RMSE penalizes large errors more strongly, and R² is the share of AQI variation explained.

## Slide 8
Part I: Feature Importance
Chart: Random Forest importance (top 6 features)
| PM2.5 | CO | PM10 | SO2 | NO | NO2
Importance | 0.401 | 0.319 | 0.089 | 0.047 | 0.046 | 0.04
PM2.5 and CO were the most important features in both the Decision Tree and the Random Forest.
In Linear Regression, CO had the largest coefficient magnitude.
All twelve features were kept, because the analysis did not justify removing any of them.
Importance describes how a model uses its inputs. It does not prove that a pollutant causes a change in AQI.

## Slide 9
Part II: Next-Day AQI Method
Feature | Description
AQI_lag_1 | AQI one day earlier
AQI_lag_2 | AQI two days earlier
AQI_lag_3 | AQI three days earlier
AQI_lag_7 | AQI seven days earlier
AQI_rolling_mean_3 | Mean AQI over three days
AQI_rolling_mean_7 | Mean AQI over seven days
A separate Random Forest model was trained for each of six cities: Bengaluru, Chennai, Hyderabad, Delhi, Mumbai, and Chandigarh.
Each city dataset was ordered by date, and the lag features and rolling means were calculated from its past AQI values.
RandomizedSearchCV selected the hyperparameters for each city.
The final model predicts the AQI of the day after the latest record.

## Slide 10
Part II: Results by City
City | CV MAE | Test MAE | Test RMSE | Test R²
Bengaluru | 20.56 | 9.19 | 12.40 | 0.600
Delhi | 45.57 | 32.75 | 44.66 | 0.846
Hyderabad | 18.26 | 11.35 | 15.35 | 0.814
Mumbai | 20.86 | 11.80 | 18.08 | 0.825
Chandigarh | 31.06 | 12.44 | 15.69 | 0.223
Chennai | 26.98 | 18.13 | 26.04 | 0.475
CV MAE is the best cross-validation error found during tuning.
Delhi had the highest test R² (0.846), but also the largest absolute errors.
Bengaluru had the lowest test MAE (9.19), although its R² was 0.600.
Chandigarh had an MAE of 12.44 but the weakest R² (0.223).
These differences show why more than one metric is needed.

## Slide 11
Part II: Tuned Hyperparameters
City | n_estimators | max_depth | max_features | min_samples_split | min_samples_leaf | bootstrap
Bengaluru | 50 | 5 | 0.7 | 8 | 10 | True
Delhi | 75 | None | 1.0 | 10 | 8 | True
Hyderabad | 150 | None | 1.0 | 15 | 8 | True
Mumbai | 125 | 15 | 0.7 | 10 | 8 | False
Chandigarh | 150 | 30 | 1.0 | 10 | 2 | True
Chennai | 50 | 5 | 0.7 | 8 | 10 | True
Each city has its own optimized settings, which reflects the differences in how AQI behaves across cities.

## Slide 12
Limitations and Future Work
Limitations
The pollutant-based models estimate AQI but do not forecast it.
The data ends in 2020 and includes the COVID-19 lockdown period.
Lag features cannot capture sudden changes caused by weather or emissions.
Feature importance and correlation do not prove cause and effect.
Future work
Add weather variables such as temperature, humidity, wind speed, and rainfall.
Compare the city-wise models with a single pooled model.
Test other time-series forecasting methods.
Extend the analysis to more cities and newer data.

## Slide 13
Conclusion
Random Forest gave the best pollutant-based estimates, with an MAE of 20.54, an RMSE of 40.31, and an R² of 0.911.
PM2.5 and CO were the most important features in the tree-based models.
Six city-wise Random Forest models were built for next-day AQI prediction, and their performance varied from city to city.
Together, the two parts show how AQI can be estimated from pollutants and forecast from past AQI values.
Thank you